## Slide 1: Modern imaging techniques in biology
The physical background of medical tomographies
Lecture 3

## Slide 2: MRI thematics
Microscopic and macroscopic magnetization. The Bloch equation. T1 and T2 relaxation times.
Magnetic resonance. 90° pulse. FID: free induction decay. Effective T2.
Pulse method for determining T2 and T1. Spin echo. Magnetic resonance spectroscopy.
Imaging. Selective excitation and read out of a slice.
Pulse sequences and contrast. Flow in MRI.
fMRI. BOLD. Echo planar imaging (EPI). Spin echo (SE) and gradient echo (GE) for fast imaging.
Image: http://radiologia.blog.hu

## Slide 3: Microscopic magnetization
Magnetic nuclei in biology: 1H, 13C, 14N, 19F, 23Na, 31P, 39K. These are stable isotopes. Most frequent: 1H = proton = p+.
Those nuclei have a non zero spin that posses unpaired proton or neutron.
Mass | Element | Magnetic dipole moment[7][8] (nuclear magnetonunits) | Nuclear spin number[7] | g-factor[9] | Larmor frequency (MHz/tesla) | Gyromagnetic ratio[10] (rad s−1 µT−1) (free atom) | Isotopic abundance | NMR Sensitivity[2] (relative to 1H)
1 | H | 2.79284734(3) | 1/2 | 5.58569468 | 42.6 | 267.522208 | 99.98% | 1
2 | H | 0.857438228(9) | 1 | 0.857438228 | 6.5 | 41.0662919 | 0.02% | 
7 | Li | 3.256427(2) | 3/2 | 2.1709750 | 16.5 | 103.97704 | 92.6% | 
13 | C | 0.7024118(14) | 1/2 | 1.404824 | 10.7 | 67.28286 | 1.11% | 0.016
14 | N | 0.40376100(6) | 1 | 0.40376100 | 3.1 | 19.337798 | 99.63% | 0.001
19 | F | 2.628868(8) |  | 5.253736 | 40.4 | 251.6233 | 100.00% | 0.83
23 | Na | 2.217522(2) | 3/2 | 1.4784371 | 11.3 | 70.808516 | 100.00% | 0.093
31 | P | 1.13160(3) | 1/2 |  | 17.2 | 108.394 | 100.00% | 0.066
39 | K | 0.39147(3) | 3/2 | 0.2610049 | 2.0 | 12.500612 | 93.1% | 
Nuclear magnetic moment, Wikipedia

## Slide 4: Spin: instrinsic angular momentum
Spin is the intrinsic angular momentum of an elementary particle, e.g., electron, proton or neutron. All of them have a spin of in
Angular momentum:
The definition of angular momentum for a point particle is a pseudovector r×p, the cross product of the particle's position vector r(relative to some origin)

## Slide 5: The origin of magnetic moment
Magnetic moment of a charged particle arises from its angular momentum:
,
where is the so-called gyromagnetic ratio. Gyromagnetic ratio of the electron:
,
where is the dimensionless (unitless) g factor of the electron. is the Bohr magneton. We would expect for a „classical” electron.

## Slide 6: g factor of the electron
The real g factor of the free electron can be theoretically calculated on the basis of relativistic quantum field theory of electromagnetism: quantum electodynamics (QED):
,
where is the fine-structure constant:

## Slide 7: g factor of the proton and the neutron
Case of the proton and neutron is similar to electron. For proton:
,
where is the gyromagnetic ratio and is the g factor of proton. is the nuclear magneton.
1 up and 2 down quarks make up the neutron. Electric charge of the up and down quarks: and .

## Slide 8: Nuclear vs electron magnetic moment
As the mass of proton is ~2000 times larger than that of electron, the magnetic moment of the proton or neutron or generali the nuclei is 3 orders of magnitude lower than that of the electron:

## Slide 9: Nuclear magnetic moment in external field
Energy (H) of a magnetic moment () in an external magnetic field (B):
The magnitude of the nuclear spin (spin quantum number I) is the eigenvalue of the operator I2
(e.g. for the proton and for 23Na ) and the component parallel to the magnetic field m is the eigenvalue of the operator Iz:

## Slide 10: Macroscopic magnetization
Spin ensemble in an external magnetic filed (B): a large number of particles with spin . Possible energy levels (discrete energy states):
A change in such a level always entails the absorption or emission of a photon
= Em-1 - Em= z

## Slide 11: High temperature: 37 °C = 310 K, lot of spins
As the number of spins (nuclei) is large, 1 mm3 contains 6.7·1019 protons and the temperature is high we can consider the Boltzmann statistics:
k is the Boltzmann constant.
Fig. 5.2 Occupation of the energy states of a spin ensemble for according to the Boltzmann distribution.

## Slide 12: Macroscopic magnetization
Magnetic moment of the sample containing N spins:
This is Curie’s law. When normalized with the volume of the sample (voxel):

## Slide 13: The Bloch equations 1
Dynamics of a magnetic moment m in a B external magnetic field:
As the torque:
This results in an infinite precession of the nuclear magnetization around the direction of the external magnetic field with a Larmor frequency:
Precession, Wikipedia

## Slide 14: The Bloch equations 2
In reality the macroscopic magnetization of the sample will return to its thermal equilibrium after excitation instead of infinite precession. The equation of motion can be amended with two empirical relaxation terms:
T1 and T2 relaxation demo video

## Slide 15: Origin of the relaxation times T1 and T2
Relaxation processes are irreversible thermal effects.
T1: longitudinal or spin-lattice relaxation
Energy transfer between the spins and their environment. Energy dissipation occurs.
T2: transverse or spin-spin relaxation
No energy transfer to the environment of the spins. Transverse component of the angular momentum gets lost as the coherence disappears due to local. This is an entropy effect.

## Slide 16: Origin of the relaxation times T1 and T2
„The relaxation times express the mobility of the molecules in which the nuclei under consideration are located.”
The stochastic nature of molecular motions is described by the autocorrelation function: K(t).
„This is a measure of how long a molecule can ’remember’ colliding with another molecule.” K(t) can be usually approximated by an exponential decay:
is the correlation time.

## Slide 17: Origin of the relaxation time T2
T2 can be described by the dephasing of the transverse component (Ix,Iy) of spins. Spins rotate with the Larmor frequency:
However, due to thermal molecular motions local Bz acting on spins fluctuates in time. The amplitude of fluctuation is described by bz. Thus different nuclei in different molecules will have a slightly different Larmor frequency. Rotation of spins with different frequencies leads to dephasing:

## Slide 18: Origin of the relaxation time T1
z component of the spins is flipped during relaxation to the thermal equilibrium. The transition probablity between two neighboring energy levels as a result of the fluctuating local magnetic field b: